## Slide 1
TEAM NISHKARSH
SMART KOPARGOAN HACKATHON
CleanKop AI
AI, IoT & GPS-Based Smart Garbage Collection and Monitoring System
PROBLEM STATEMENT ID
SKH21
PROBLEM STATEMENT TITLE
GPS-Based Smart Garbage Collection and Monitoring System
THEME
Open Innovation
PS CATEGORY
Software
TEAM ID
T4M4VZ
TEAM NAME
Team Nishkarsh
Team Members: Parth Desai (Leader) • Divya Pawar • Shreyash Patil • Tanavi Pawar

## Slide 2
Team Nishkarsh
IDEA TITLE
CleanKop AI — Proposed Solution
A unified IoT + AI platform that gives every bin a digital identity, every collection route a data-driven plan, and every citizen complaint a transparent trail — replacing today's manual, fixed-schedule waste collection.
PROBLEMS WE SOLVE
No real-time fill data — collections run on fixed schedules, not actual need
No centralized tracking — zero accountability or data synchronization
No digital complaints — issues stay informal, untracked, unprioritized
No feedback loop — performance is never measured or improved
HOW CLEANKOP AI ADDRESSES IT
Ultrasonic + ESP32 sensors report live bin fill % over Wi-Fi/GSM
TSP nearest-neighbor + 2-opt engine plans the shortest priority route
Citizen app + ticketed complaints with Submitted → Resolved workflow
Live admin dashboard tracks fuel saved, resolution time & performance
CleanKop AI | Team Nishkarsh | Smart Kopargoan Hackathon
2

## Slide 3
Team Nishkarsh
TECHNICAL APPROACH
Technology Stack & Methodology
Frontend
React.js + Tailwind CSS
Backend
Node.js + Express
Database
MongoDB / PostgreSQL + PostGIS
Maps
Leaflet.js + OpenStreetMap
Real-time & Alerts
Socket.io, Nodemailer / Twilio
Hosting
Vercel + Render + Mapbox APIs
IMPLEMENTATION METHODOLOGY
1
Sensor → Cloud
ESP32 + ultrasonic sensor sends fill-level data to the backend every few minutes (hackathon: simulator script)
→
2
Store & Alert
Backend stores bin data in the database; bins over 80% trigger an automatic alert
→
3
Optimize Route
TSP nearest-neighbor + 2-opt algorithm ranks red/yellow/green bins and outputs the shortest route
→
4
Collect & Update
Driver app tracks GPS live and marks bins collected; status syncs to admin in real time
→
5
Resolve Complaints
Citizen reports flow through Submitted → Assigned → In Progress → Resolved, with 48-hr escalation
CleanKop AI | Team Nishkarsh | Smart Kopargoan Hackathon
3

## Slide 4
Team Nishkarsh
TECHNICAL APPROACH
System Architecture
HOW TO READ IT
IoT layer
Bin sensors + ESP32 push fill data to the backend
Backend core
Node.js/Express handles auth, routing, complaints, alerts
Data layer
MongoDB/PostgreSQL + PostGIS stores bins, routes, users
Three apps
Citizen, Admin & Driver apps share one live backend
Route engine
TSP + 2-opt turns priority bins into an optimized path
CleanKop AI | Team Nishkarsh | Smart Kopargoan Hackathon
4

## Slide 5
Team Nishkarsh
FEASIBILITY AND VIABILITY
Can We Build & Run This?
FEASIBILITY
ESP32 + ultrasonic sensors are low-cost, off-the-shelf, and hackathon-ready
Full stack (React, Node.js, MongoDB/PostgreSQL) is mature, documented, and free to prototype on
TSP nearest-neighbor + 2-opt is lightweight enough to run on a standard server in real time
Firmware-ready architecture: today's simulator script swaps for real sensors with no redesign
RISKS → MITIGATION STRATEGY
Per-bin hardware cost
Phase rollout — pilot in a few high-traffic wards before city-wide scale-up
Patchy rural connectivity
GSM fallback alongside Wi-Fi so bins report even without broadband
Driver / citizen adoption
Simple mobile-first apps + training and incentive program for drivers
Sensor data accuracy
Threshold smoothing + manual override option in the admin dashboard
CleanKop AI | Team Nishkarsh | Smart Kopargoan Hackathon
5

## Slide 6
Team Nishkarsh
IMPACT AND BENEFITS
Who Gains, and How
Target audience: Kopargaon municipal corporation, sanitation drivers, and citizens across the city.
Efficient Collection
Priority routing (red → yellow → green bins) cuts wasted trips
Reduced Fuel Cost
20–30% distance saved vs. fixed manual routes
Clean & Healthy City
Bins emptied before overflow — fewer health & odor complaints
Real-time Monitoring
Admins see live fill levels, trucks, and complaints on one map
Data-Driven Decisions
Analytics and heatmaps guide staffing and future bin placement
Citizen Satisfaction
Transparent ticket status builds trust in the system
CleanKop AI | Team Nishkarsh | Smart Kopargoan Hackathon
6

## Slide 7
Team Nishkarsh
RESEARCH AND REFERENCES
Grounded in Established Tools & Methods
ESP32 + Ultrasonic Sensing
Espressif ESP32 technical reference & HC-SR04 ultrasonic sensor documentation for bin fill-level sensing
Route Optimization
Traveling Salesman Problem — Nearest-Neighbor construction heuristic refined with 2-opt local search
Geospatial Data
PostgreSQL + PostGIS documentation for storing and querying bin/route geo-coordinates
Mapping & Live Tracking
Leaflet.js and OpenStreetMap documentation for the live map and route rendering
Real-time Communication
Socket.io documentation for live GPS updates, bin alerts, and dashboard sync
Reference Municipal Models
Smart-city solid-waste-management case studies (IoT bin sensors + optimized collection routing)
CleanKop AI | Team Nishkarsh | Smart Kopargoan Hackathon
7

## Slide 8
Team Nishkarsh
RESEARCH AND REFRENCES
DETAILS
CleanKop AI | Team Nishkarsh | Smart Kopargoan Hackathon
8
ESP32 & Ultrasonic Sensor
  Espressif Systems. ESP-IDF Programming Guide (Official Documentation).
  HC-SR04 Ultrasonic Sensor Datasheet (Components101 / Manufacturer Documentation).
Route Optimization
  Traveling Salesman Problem (TSP): Nearest Neighbor + 2-Opt Heuristic.
  MDPI, Applied Sciences (2023).
Geospatial Database
  PostgreSQL + PostGIS Official Documentation.
Live Mapping
  Leaflet.js Official Documentation.
  OpenStreetMap Documentation.
Real-Time Communication
  Socket.IO v4 Official Documentation
  .
Real-World Smart Waste Management Case Studies
  Mumbai (Malad), India – IoT Smart Bin Deployment (IIETA Journal): ~20% reduction in garbage truck usage
Team Members: Parth Desai (Leader) • Divya Pawar • Shreyash Patil • Tanavi Pawar